## Slide 1
A 2.1.3 | IB Computer Science
Network
Devices
Modems · Routers · Switches · NICs · WAPs · Gateways · Firewalls
Learning Intention: Describe the function of network devices and map them to the TCP/IP model.

## Slide 2
⏱ DO NOW ACTIVITY
5 Minutes — Think & Respond
5 min
📋 Your Tasks
L1
Name THREE devices you use at home or school that help you connect to the internet.
L2
Explain the difference between a router and a switch. What does each one do?
L3
Reflect: If a router failed in your school, what would happen? Which devices would be affected and why?
TOK
Do we truly understand the technology we depend on — or do we simply trust it to work without knowing how?
Learning Intention: Describe the function of network devices and understand how they map to the layers of the TCP/IP model.

## Slide 3
NETWORK DEVICES
Modems & Routers
📡 Modem
MOdulator / DEModulator
🔧 Function
Translates digital signals from your devices into analogue signals for telephone/cable lines — and back again.
🌐 Role
Bridges your local network to the wider internet. The 'translator' between home and ISP.
📍 TCP/IP Layer
Network Access (Link) Layer — handles physical signal transmission over the network medium.
💡 Example
ADSL modem, cable modem, fibre ONT (optical network terminal).
🔀 Router
Traffic controller of your network
🔧 Function
Receives data packets from the modem and directs them to the correct device using IP addresses.
🌐 Role
Manages network traffic between devices. Like a central hub with multiple roads to different destinations.
📍 TCP/IP Layer
Network Layer — routes packets between networks using IP addresses to find the best path.
💡 Example
Home Wi-Fi router, enterprise Cisco router, ISP core router.

## Slide 4
NETWORK DEVICES
Switches & Network Interface Cards (NICs)
🔌 Switch
The mailroom of your network
🔧 Function
Connects multiple devices within a LAN and directs data packets only to the intended recipient — using MAC addresses.
🌐 Role
Reduces unnecessary traffic by sending data only to the addressed device — like a mailroom sorting mail.
📍 TCP/IP Layer
Network Access (Link) Layer — operates using MAC addresses within a local network.
💡 Example
24-port office switch, managed enterprise switch, PoE switch.
🖥 Network Interface Card (NIC)
The doorway into the network
🔧 Function
Provides the physical interface for a device to connect to a network — wired (Ethernet) or wireless.
🌐 Role
Every networked device needs a NIC. It's the doorway that lets a device 'enter' the network.
📍 TCP/IP Layer
Network Access (Link) Layer — provides the hardware interface between device and network medium.
💡 Example
Built-in Ethernet port on a laptop, PCIe network card, USB Wi-Fi adapter.

## Slide 5
NETWORK DEVICES
Wireless Access Points (WAPs) & Gateways
📶 Wireless Access Point (WAP)
The radio tower of your network
🔧 Function
Broadcasts a wireless (Wi-Fi) signal that devices can detect and connect to — creating a wireless network.
🌐 Role
Extends a wired network to wireless devices. Acts like a radio tower transmitting signals.
📍 TCP/IP Layer
Network Access (Link) Layer — provides wireless access using 802.11 (Wi-Fi) standards.
💡 Example
School Wi-Fi access point, Cisco WAP, ceiling-mounted enterprise AP.
🔗 Gateway
The border crossing between networks
🔧 Function
Bridges two different networks with incompatible protocols — translating data formats so they can communicate.
🌐 Role
Acts like a border crossing: checks and translates between two 'countries' with different languages/rules.
📍 TCP/IP Layer
Operates at MULTIPLE layers — translates protocols across Application, Transport & Network layers as needed.
💡 Example
VoIP gateway (phone ↔ internet), cloud gateway, IoT gateway.

## Slide 6
NETWORK DEVICES
Hardware Firewalls
🔒 What is a Hardware Firewall?
The security guard of your network
🔧 Function
Examines all incoming and outgoing network traffic — blocking unauthorised access and malicious activity.
🌐 Role
Acts as a physical barrier between your internal network and the outside world, protecting devices and data.
📍 TCP/IP Layer
Operates at MULTIPLE layers — filters by IP address (Network), port (Transport), and protocol (Application).
💡 Example
Cisco ASA firewall, Fortinet FortiGate, WatchGuard Firebox, pfSense appliance.
🛡 What Does It Filter?
IP Addresses
Block or allow traffic from specific source or destination IPs.
Ports
Restrict access to specific ports (e.g. block port 23 Telnet, allow 443 HTTPS).
Protocols
Filter based on protocol type — TCP, UDP, ICMP etc.
Packet Inspection
Deep packet inspection examines the content of data packets for malicious payloads.
Stateful Tracking
Tracks connection states — only allows responses to legitimate outbound requests.

## Slide 7
THE TCP/IP MODEL
Understanding the Four Layers
4
Application Layer
Deals with user applications & services — web browsers, email clients, FTP programs. Where users interact.
3
Transport Layer
Ensures reliable data delivery between applications. Handles segmentation, flow control & error checking (TCP/UDP).
2
Network Layer
Handles logical addressing & routing between networks. Uses IP addresses to determine the best path for packets.
1
Network Access Layer (Link Layer)
Physical transmission of data over a specific medium (Ethernet, Wi-Fi). Defines protocols for accessing the physical network.

## Slide 8
TCP/IP MAPPING
Network Devices & Their TCP/IP Layers
Device
TCP/IP Layer
Address Used
Key Role
Modem
Network Access (Link)
Physical signal
Digital ↔ Analogue signal conversion
Router
Network Layer
IP address
Routes packets between networks
Switch
Network Access (Link)
MAC address
Directs packets within a LAN
NIC
Network Access (Link)
MAC address
Physical interface for network connection
WAP
Network Access (Link)
MAC address
Wireless access via 802.11 (Wi-Fi)
Gateway
Multiple layers
Various
Translates protocols between networks
Firewall
Multiple layers
IP / Port / Proto
Filters & blocks unauthorised traffic

## Slide 9
KEY COMPARISONS
Modem vs Router vs Gateway
📡 Modem vs Router
Modem
Connects your network to the ISP/internet — converts digital to analogue signals.
Router
Manages traffic WITHIN your network — directs packets to the right device using IP addresses.
Key Diff
Modem = connects to internet. Router = manages internal network. You need BOTH together.
🔗 Router vs Gateway
Router
Routes packets between networks using IP addresses — typically same protocol family.
Gateway
Bridges DIFFERENT networks with INCOMPATIBLE protocols — full protocol translation needed.
Key Diff
Gateway is more powerful: it translates between entirely different network types and protocols.

## Slide 10
IB DIFFERENTIATED ACTIVITIES
Exam-Style Questions — 20 Minutes
ACCESS
AO1 · Recall & Define
APPLY
AO2 · Explain & Analyse
EVALUATE
AO3 · Justify & Discuss
Q1 (3 marks)
A student at home wants to connect their laptop to the internet.
(a) Identify the device that converts digital signals to be sent over a telephone line. [1]
(b) State TWO functions of a router in a home network. [2]
Q2 (4 marks)
A school network has 200 computers connected via switches with one router to the internet.
(a) Explain why switches are used instead of connecting all devices directly to the router. [2]
(b) Identify the TCP/IP layer that switches operate at and explain why. [2]
Q3 (5 marks)
A business connects its office LAN to a hospital's different network system.
(a) Identify the device most suitable for this connection. [1]
(b) Explain why this device must operate at multiple TCP/IP layers. [2]
(c) Evaluate whether a router alone could perform this role. [2]

## Slide 11
HL STRETCH | EXTENSION ACTIVITIES
Analyse · Evaluate · Justify
Q4 (6 marks) — AO3 — Evaluate
A company is upgrading its network security and is choosing between a software firewall and a hardware firewall.
(a) Describe TWO differences between a software and hardware firewall. [2]
(b) Evaluate which solution better suits a company network with 500 employees, justifying your answer with reference to TCP/IP layers. [4]
Q5 (6 marks) — AO3 — Justify
A smart factory connects traditional machinery to a cloud-based monitoring system using IoT sensors.
(a) Identify the network device needed to bridge the factory's legacy network to the internet system. [1]
(b) Explain why this device must operate at multiple TCP/IP layers. [2]
(c) Justify whether a router and a WAP alone could replace this device. [3]

## Slide 12
PLENARY
Match the Device to Its Function
1
Converts digital signals to analogue and back again — connecting your local network to the internet.
2
Directs data packets only to the intended device within a LAN using MAC addresses, reducing traffic.
3
Creates a Wi-Fi network by broadcasting a wireless signal that nearby devices can detect and join.
4
Acts as a border crossing between two networks with incompatible protocols — translating both data formats and languages.
A. Modem
B. Switch
C. WAP
D. Gateway